Sample Calculations for lab 05
Be sure to follow through with correct units in your calculations at each step.

A spring has a spring constant of 5 N/m.
(1) if a 0.1 kg mass is attached to the spring, how much will the spring stretch?
(2) Suppose two of these springs are connected in series. Calculate the effective spring constant.
(3) Suppose two of these spring are connected in parallel. Calculate the effective spring constant.
(4) A point mass m=1 kg is rotating with a constant at a radius of 0.1 m, calculate the tangential velocity of the system if the centripetal force is 2 N.